## Slide 1
LYRA
Wearable Music Interface
A glove-based musical instrument for the modern musician
Andrew McKnight · HCI Lead
Maanav Allampallam · Communications Lead
Shaan Yadav · Hardware Lead
Christian Bepler · Software Lead
ECE 469 · Final Presentation · 2026

## Slide 2
Motivation & Contribution
The Problem
Musical instruments are expensive and bulky. Musicians can't explore multiple instruments affordably, and inspiration strikes when instruments aren't available.
Why Now
Miniaturized sensors (IMU, flex) and BLE SoCs are cheaper and smaller than ever, enabling a wearable instrument that fits in a pocket.
Who Benefits
Aspiring musicians exploring instruments without financial commitment. Touring musicians who can't bring every instrument. Anyone who needs to practice on the go.
Our Contribution
A single-glove wearable that translates hand gestures and finger flexion into musical notes — one device, multiple instruments, no cost barrier.

## Slide 3
MVP Requirements
✓ MINIMUM VIABLE PRODUCT
1
Wearable Glove Device
Flex sensors on all 5 fingers + BLE SoC (Seeed Xiao Sense) embedded in a fabric glove
2
Laptop Web App
Receives sensor data over BLE WebBluetooth API; renders UI and generates sound in-browser
3
3 Distinct Musical Functions
Finger flex → note trigger; gyroscope → pitch/expression; multi-finger chords
★ STRETCH GOALS
✓
Multiple Instrument Types
Piano, drum pads, theremin-style pitch control — selectable in-app
✓
User-Customizable Bindings
Freely bind any finger or gesture to any note, chord, or instrument parameter
○
Reduced Form Factor
PCB integration to shrink the circuit footprint; battery on glove
○
Two-Glove Expansion
Second glove with inter-glove BLE communication for richer expression
✓ Achieved ○ Not yet implemented

## Slide 4
System Architecture
HARDWARE
SOFTWARE
Flex Sensors
(×5, one per finger)
IMU / Gyroscope
(LSM6DS3, 6-axis)
LiPo Battery
(3.7V, portable)
Seeed Xiao
BLE Sense
• Reads ADC (flex)
• Reads IMU
• Formats CSV
• Transmits via
BLE UART NUS
MCU
BLE
Python
Receiver
(BLE → HTTP POST)
FastAPI/uvicorn
Server
(/sensor + /ws)
Web App
(Tone.js, sound
generation + UI)

## Slide 5
Technical Deep Dive: BLE Communication Pipeline
Challenging module: Real-time, low-latency wireless sensor streaming over Bluetooth Low Energy
1
ADC + IMU Sampling
Seeed Xiao Sense reads 5 flex sensor ADCs at 12-bit precision and IMU (Gx, Gy, Gz, Ax, Ay, Az) via I2C. Raw IMU data is fused via a complementary filter (α=0.98) into Roll/Pitch/Yaw before transmission. Key fix: default 10-bit ADC divided resistance range by 4 — switching to 12-bit precision fixed missed bend detection.
2
CSV Formatting & BLE TX
Data serialized as comma-separated ASCII: 'ROLL,PITCH,YAW,ACCEL_MAG,R0,...,R4\n' (complementary-filter angles in degrees + flex resistances in Ω). Transmitted via Nordic UART Service (NUS) over BLE at 100 Hz. BLE connection interval set to 7.5–15 ms for low-latency response.
3
Python Receiver & FastAPI HTTP Bridge
Python script (bleak library) subscribes to NUS TX characteristic. On notification, buffers bytes and splits on newline. Parses CSV into a JSON dict and POSTs it to the FastAPI /sensor endpoint via httpx. Switched from Arduino serial (buggy) to independent Python process.
4
Web App Sound Generation
Browser connects to FastAPI WebSocket (/ws), receives sensor frames event-driven at up to 100 Hz. User-configured bindings map sensor values to notes/chords. Tone.js synthesizes audio. In digital mode: flex ≥ threshold triggers note-on per finger. In analog mode: configurable sensor axes drive pitch, volume, and timbre continuously.
Key result: Bend detection accuracy fixed by upgrading ADC to 12-bit (4095 steps vs. 1023). End-to-end latency (∼80 ms) dominated by BLE connection interval (set to 7.5–15 ms). Console print throttle (PRINT_INTERVAL) is cosmetic — all sensor packets are always forwarded to the server.

## Slide 6
BLE Receiver — Key Implementation
DEVICE_NAME = "HandMusic" NUS_TX_CHAR = "6e400003..." _buffer = "" def on_notification(sender, data: bytearray): global _buffer, _last_print _buffer += data.decode("utf-8", errors="replace") while "\n" in _buffer: line, _buffer = _buffer.split("\n", 1) line = line.strip() if line: now = time.time() # Throttle only the console print (not in data path) _send_to_server(packet) # HTTP POST to FastAPI
NUS UART characteristic UUID — standard BLE UART profile
Stream arrives in chunks — buffer + split on newline for complete frames
Print throttle (PRINT_INTERVAL) only slows console output — every packet is always forwarded to the server without delay
Each packet: 'ROLL,PITCH,YAW,ACCEL_MAG,R0,...,R4' → parsed into JSON dict, HTTP POSTed to FastAPI /sensor

## Slide 7
Prototype Demo
Live demonstration of MVP and additional functionalities
[ INSERT FINAL PROTOTYPE PHOTO OR VIDEO EMBED HERE ]
DEMO CHECKLIST
✓
MVP: Finger flex → note trigger
✓
MVP: Multi-finger chord generation
✓
MVP: Web app receives BLE in real time
✓
Extra: Customizable finger-note bindings
✓
Extra: Gyroscope pitch expression
—
Extra: Multiple instrument types
[ INSERT PRE-RECORDED VIDEO DEMO HERE ]
Replace placeholder above with embedded or linked demo video

## Slide 8
Ideal Product Vision
If we had unlimited resources and time — what Lyra becomes
Custom PCB & Miniaturization
Replace breadboard + protoboard with a purpose-built flexible PCB that conforms to the glove. Integrate BLE SoC, ADC mux, and power management on a single board weighing under 10g.
Two-Glove System
Second glove adds left-hand control. Inter-glove BLE mesh lets the left hand control effects, modulation, and octave shift while the right hand plays notes — full expressive range.
Haptic Feedback
LRA vibration motors in the fingertips provide tactile confirmation of note triggers — closing the sensory loop so the musician can "feel" their instrument.
Standalone Operation
Embedded audio DSP on the glove (e.g., RP2040 + I2S DAC) eliminates laptop dependency. Bluetooth speaker or IEM connection — fully wireless, pocketable instrument.
ML Gesture Recognition
On-device tinyML model trained on player gestures enables complex gestures (vibrato, slides, strums) mapped to expressive parameters beyond simple threshold triggers.
Instrument Marketplace
Community-driven plugin ecosystem — users share custom instrument mappings, effects chains, and gesture vocabularies. New instrument = new JSON config, not new hardware.

## Slide 9
Thank You
Questions & Discussion
Andrew McKnight · HCI Lead Maanav Allampallam · Communications Lead Shaan Yadav · Hardware Lead Christian Bepler · Software Lead
ECE 469 · Duke University · 2026